FM synthesis

deviation = index * modulator

number of sidebands ~ index + 1

k = number of sidebands on each side

spectrum density ~ 2k +1	index = 2.5 → 9 components, 8 spectral + carrier
but possible cancellations

DISSCO

fundamental frequency = carrier
rate of vibrato	= modulator
amplitude of vibrato	= deviation

f0 = fc/N1 = fm/N2	when fc / f m have large integer values → inharmonic spectrum

Good Gong:	carrier	= 60Hz	env: 13
modulator	= 125	1
amp	= 10	13

Chowning wood drum:	carrier	= 80 Hz	env:	15
modulator	= 55	1
amp	= 25	16

also	fc	= 400
       fm	= 581	ratio of 1.454545....
       amp	= 35

Clarinet:	fc	= 205	164	env:	7
fm	= 419	328	(2/1)	1
amp	= 3	13

for very low:	fc = 41	invers: ½ → rough
fm= 82